## Slide 1
High Efficiency Ammonia Electrosynthesis via Understanding
the Mass-transport Effects of Phosphonium Ionic Liquids
Trung Nguyen a, Hoang-Long Du a, Luke A. O’Dell b, Alexandr N. Simonov a ,*, Douglas R. MacFarlane a ,*
a ARC Center of Excellence for Electromaterials Science, School of Chemistry, Monash University, Clayton, Victoria 3800, Australia
b Institute for Frontier Materials, Deakin University, Geelong, Victoria 3216, Australia
Email: trung.nguyen3@monash.edu
Introduction
Conventional Haber-Bosch process
Intensive resource and energy consumption
Contribute ~2% of global CO2 emissions
NH3 electrosynthesis
Allow to occur under mild ambient conditions
Green & zero emission
Powered by renewable energy
N2 and H2O can be converted into NH3 via
electrochemical process enabled by renewable electricity
Li-mediated nitrogen reduction (Li-NRR): the most promising way to synthesize NH3 with high faradaic efficiency and prospective rates.
Common proton carrier: Ethanol
Alternative: Phosphonium-based ionic liquids with unique properties
New phosphonium-based ionic liquids as proton shuttles for the NRR
Diffusion coefficients of Li+ and phosphonium cations
in the electrolyte solution
Effects of potential at 20 bar N2
Long-term operation
Electrochemical analysis
Cyclic transformation of phosphonium IL (31P NMR)
Objectives
Investigation of the mass-transport effects of phosphonium-based
ionic liquids
Designing an effective continuous flow cell to study mass-transport
in the Li-NRR system
Kinetic modelling and simulation for discovering mechanistic insight for the Li-NRR
Lithium-mediated NRR performance
Electrochemical and control procedure
Experimental
Ammonia quantification: Spectrophotometric Berthelot method
Standard addition method: eliminate matrix interferences
Ammonia concentrations correspond to absorbance of
indophenol chromophore
[P6,6,6,14][eFAP]: a stable proton shuttle for Li-NRR
NH3 yield rate ~ 53 1 nmol s-1 cm-2 ; Faradaic efficiency ~ 69 1 % in 20h under 19.5 bar N2 & 0.5 bar H2
Continuous operation is successfully conducted in 3 days
References
1. MacFarlane, D. R.; Cherepanov, P. V.; Choi, J.; Suryanto, B. H. R.; Hodgetts, R. Y.; Bakker, J. M.; Ferrero Vallana, F. M.; Simonov, A. N., A Roadmap to the Ammonia Economy. Joule 2020, 4 (6), 1186-1205.
2. Suryanto, B. H. R.; Matuszek, K.; Choi, J.; Hodgetts, R. Y.; Du, H.-L.; Bakker, J. M.; Kang, C. S. M.; Cherepanov, P. V.; Simonov, A. N.; MacFarlane, D. R., Nitrogen reduction to ammonia at high efficiency and rates based on a phosphonium proton shuttle. Science 2021, 372 (6547), 1187-1191.
3. Choi, J.; Suryanto, B. H. R.; Wang, D.; Du, H.-L.; Hodgetts, R. Y.; Ferrero Vallana, F. M.; MacFarlane, D. R.; Simonov, A. N., Identification and elimination of false positives in electrochemical nitrogen reduction studies. Nature Communications 2020, 11 (1), 5546.
4. Lazouski, N.; Steinberg, K. J.; Gala, M. L.; Krishnamurthy, D.; Viswanathan, V.; Manthiram, K., Proton Donors Induce a Differential Transport Effect for Selectivity toward Ammonia in Lithium-Mediated Nitrogen Reduction. ACS Catalysis 2022, 5197-5208.
DOI: 10.1016/j.joule.2020.04.004
DOI: 10.1016/j.joule.2020.04.004
Reduction rate increased 10 times
Current density (mA cm-2)
Current density (mA cm-2)
EWE ( V vs. )
Time (min)
Re (Z) (kΩ)
-Im (Z) (kΩ)
Conductivity (mS cm-1)
EWE ( V vs. )
N2 pressure
Effects of N2 pressure at E = -0.75V vs.
Improved Phosphonium Proton Shuttle
Phosphonium Proton Shuttle for the NRR
2.5 M LiNTf2 in THF solvent
0.1 M ILs in LiNTf2 / THF electrolyte
Neat [P1,4,4,4] [NTf2]
Neat [P6,6,6,14] [NTf2]
DOI: 10.1126/science.abg2371
DOI: 10.1126/science.abg2371
DOI: 10.1038/s41467-020-19130-z